## Slide 1: ﻿Disentangling the Dual Role of NIC Receive Rings
Boris Pismenny* | Adam Morrison | Dan Tsafrir
*work done mostly while at the Technion

## Slide 2: Receiving packets
core1
core2
NIC
Rx2
Rx1
memory
Notes: Software and NICs interact via logically cyclic arrays called rings. NIC receive ring entries point to empty MTU sized buffers ready to store packets. Multi-core systems employ a receive ring per-core to scale packet reception capacity. The NIC distributes incoming packets between multiple rings according to a hash on packet headers. In this presentation, we will use the following running example. We have two cores receiving packets: core 1 in blue, and core 2 in pink <click>. Each core has a receive ring with buffers marked with the corresponding color <click>. These receive rings reside in host memory <click>.

## Slide 3: The I/O working set problem
LLC
😔
Chart: 
| 64 | 128 | 256 | 512 | 1Ki | 2Ki
Throughput | 195.6 | 195.2 | 175.1 | 170.7 | 165.4 | 157.9
throughput (Gbps)
DDIO
(20% of LLC)
LLC
DRAM
ring size (entries)
20%
15%
Notes: By default, in 100 Gbps NICs, Rx rings are sized to have 1024 buffers each large enough to store an MTU-sized packet. Consequently, the I/O working set, that is the size of all Rx rings is typically greater than the per-core LLC <click>. As a result, high-performance network applications cannot benefit from optimizations such as DDIO that enable serving NIC DMA from the LLC <click>. Consequently, the performance of these applications will decline. To demonstrate the cost of a large working set, we run an experiment with a synthetic network function that receives packets, accesses memory twice per packet, performs routing and sends packets out to the wire. We run this NF on all CPU cores, and we load it with 200Gbps using an open loop load generator <click>. The following figure shows throughput in Gbps as a function of ring size. We see that rings smaller than 256, <click> whose working set fits into the DDIO portion of the LLC, achieve line-rate 200 Gbps throughput. Next, we see that rings smaller than 1024, <click> which fit in the LLC but not in DDIO’s portion of the LLC have up to 15% lower throughput <click>. Finally, with rings of 1024 entries, which is the default size, or larger, the working set exceeds the LLC, and all data goes through DRAM resulting in up to 20% throughput degradation <click>. The takeaway from this is that shrinking receive rings may benefit applications performance.

## Slide 4: Reduce set – multicore
LLC
🤓
Chart: 
| 64 | 128 | 256 | 512 | 1Ki | 2Ki | 4Ki
Multicore | 97.2463 | 97.2463 | 97.1213 | 97.2638 | 97.2887 | 97.16 | 97.26
no-drop throughput (Gbps)
multicore
ring size (entries)
Notes: At first glance, it appears that one may reduce the size of Rx rings to fit the I/O working set in the LLC and even in DDIO’s portion of the LLC <click>. This approach works well when traffic is evenly spread across multiple cores. For example, we run DPDK’s l3fwd app and measure the maximum throughput without packet loss for various ring sizes <click>, and when traffic is spread among multiple cores, we indeed see that we can reach 100Gbps with any ring size, including the smallest 64 entry Rx ring support by NVIDIA NICs.

## Slide 5: Reduce set – single core
LLC
😔
Chart: 
| 64 | 128 | 256 | 512 | 1Ki | 2Ki | 4Ki
Multicore | 97.2463 | 97.2463 | 97.1213 | 97.2638 | 97.2887 | 97.16 | 97.26
Single core | 28.4913 | 43.1583 | 60.18 | 69.7 | 83.9725 | 83.4463 | 84.9938
single core
The default works best
ring size (entries)
multicore
no-drop throughput (Gbps)
Notes: But, reducing the size of rings doesn’t always work. When traffic is bursty, such as when several flows arrive at a single core <click>, then larger buffers are necessary to absorb these bursts. We repeat the previous experiment using a single core this time <click>. The results show that small rings are unable to absorb bursts and therefore result in packet loss and lower no-drop throughput. We can also see that the default 1024 ring size work best <click>, and that larger than default rings show no benefit.

## Slide 6: ShRing [OSDI ’23]
LLC
🤓
LLC
🤓
single core
multi- core
Notes: In OSDI 2023, we presented shRing, an alternative receive ring architecture that efficiently shares receive ring buffers across several cores. By sharing buffers, shRing absorbs bursts directed at a single core <click>, while also fitting the I/O working within the LLC in multicore workloads <click>. Although synchronization on a shared receive ring incurs overhead, in shRing we have shown that it may be preferable to spilling beyond the LLC.

## Slide 7: ShRing [OSDI ’23]
LLC
😔
multi- core
drop!
λ > μ
λ < μ
λ (arrival rate)
μ (service rate)
queueing theory
imbalance
Notes: The main problem with shRing is that due to a lack of isolation between cores. When the arrival rate exceeds the service rate, queueing theory dictates, that the queue overflows. What this means for shRing <click> is that when packets arrive from the network, and one core’s arrival rate is greater than its service rate <click>, then the ring fills up with packets waiting to be processed by the overloaded core <click>, resulting in packet loss for all cores sharing the ring <click>. To address this issue with shRing, we had to resort to using heuristics to identify imbalance and fall back to the baseline.

## Slide 8: Intermediate summary
LLC
😔
single core
LLC
😔
multi- core
drop!
λ > μ
λ < μ
(2) problematic to share buffers
(1) problematic to reduce size
Notes: Let’s summarize what we’ve seen so far. On the one hand <click>, it is problematic to reduce ring size as it results in packet loss when traffic is bursty. And on the other hand <click>, it is problematic to share buffers as load imbalance results in packet loss. So, what can we do to address this problem?

## Slide 9: Claim: caused by allocation/reception entanglement(2 producer-consumer pairs)
producer
consumer
consumer
producer
same Rx ring
lockstep progress
allocate empty buffers
receive full buffers
Notes: We claim that this problem is caused by an entanglement of two pairs of producer-consumer structures in each receive ring: one for allocation and another for reception. In one <click>, the CPU produces empty buffers for the NIC to consume. In the other <click>, the NIC produces packets for the CPU to consume. Since this is the same NIC and CPU, and most importantly the same Rx ring for both structures, packet processing advances in lockstep <click>. In other words, progress in the packet reception consumer-producer structure necessitates progress in the buffer allocation consumer-producer structure.
---
- two producer-consumer "pairs"
emphasize the lockstep behaviour
emphasize that it's the same core and the same nic not only the same ring

## Slide 10: RxBisect: disentangles Rx into two independent rings
producer
consumer
allocate empty buffers
consumer
producer
receive full buffers
different rings
Ax
Bx
Notes: To solve this problem, we propose RxBisect, which disentangles the two producer-consumer structures of receive rings into separate rings. We call one ring Ax <click>, which stands for allocation ring, and it consists of empty buffers produced by the CPU and consumed by the NIC. We call the other NIC Bx, which stands for bisected reception ring, and it contains packets produced by the NIC and consumed by the CPU.

## Slide 11: RxBisect: disentangles Rx Bx is empty unless packets are pending
producer
consumer
allocate empty buffers
consumer
producer
receive full buffers
different rings
Ax
Bx
Notes: Note that the Ax ring is always kept full of buffers by the CPU, while the Bx ring is typically empty <click>, as the CPU drains it from buffers as soon as possible. The reason Bx is mostly empty is rooted in queuing theory, which dictates that as long as the service rate exceeds the arrival rate, no long-standing queues are formed.
- explain that Ax determines the working set, and it can be made smaller (next slide)

## Slide 12: RxBisect: disentangles Rx Ax can be smaller than Bx
producer
consumer
allocate empty buffers
consumer
producer
receive full buffers
different rings
Ax
Bx
Notes: Since the size of the Ax ring determines the I/O working set size, we can reduce the I/O working set by shrinking Ax rings <click>. And to absorb bursts, we share the buffers of Ax rings while Bx rings remain as large as the default ring <click>. The takeaway is that by disentangling the two producer-consumer mechanisms, we address both the I/O working set problem and the single bursty flow problem.

## Slide 13: RxBisect: single core NIC may use any Ax to feed any Bx (same app)
Ax1
Bx1
Ax2
Bx2
Notes: The following animation demonstrates how Bx rings share Ax ring buffers. Suppose we have two cores of the same application: blue and pink, which use RxBisect. Suppose that the blue core suddenly receives a burst of traffic <click>, for instance because traffic from the other core shifted to it. Now, as packet arrive from the network, the Bx ring of the blue core first consumes the buffers of the Ax ring of the blue core <click>. Then, when the buffers of the blue core’s Ax ring run out, it consumes the buffers of the other core’s Ax ring <click>. In our design, we match the size of Bx rings to the sum of all Ax rings that provide it with buffers. In this case, two cores with Ax rings of two buffers, result in Bx rings with four buffers.

## Slide 14: RxBisect: multicore each Ax preferably serves its Bx
Ax1
Bx1
Ax2
Bx2
Notes: When traffic is spread evenly between cores, local per-core buffers are sufficient, and each Bx ring consumes buffers from its local Ax ring <click> without sharing or borrowing buffers.

## Slide 15: RxBisect vs. ShRing
 | can handle imbalanced load
ShRing | 😔
RxBisect | 🤓
Notes: Next we summarize the differences between RxBisect and ShRing. First, as we’ve seen in the previous slides, shRing can’t handle imbalanced load, as one overloaded core will slow down all other cores sharing a ring. In contrast, in RxBisect, imbalanced load impacts only the overloaded core, while other cores make progress with their Ax and Bx rings unimpeded.

## Slide 16: RxBisect vs. ShRing
 | can handle imbalanced load | software-side sync overhead for sharing
ShRing | 😔 | 😔
RxBisect | 🤓 | 🤓
Notes: Second, shRing necessitates locking in software to synchronize over shared data structures, which increases packet processing latency. In contrast, in RxBisect, cores make progress independently of other cores and with no additional overhead relative to the baseline ring per-core model.

## Slide 17: RxBisect vs. ShRing
 | can handle imbalanced load | software-side sync overhead for sharing | HW changes
ShRing | 😔 | 😔 | 🤓
RxBisect | 🤓 | 🤓 | 😔
*shRing HW was also not supported when we started working on it
Notes: One benefit shRing has over RxBisect is that it is already available with current hardware, whereas RxBisect necessitates hardware changes.

## Slide 18: Implementation
Emulate the NIC interface in software
Run the emulator on another NUMA node
Capture DDIO effects for packet buffers
Emulator also supports privRing and shRing
Emulator throughput up to 12% lower than non-emulated throughput
QPI
NUMA 0
(workers)
NUMA 1
(emulator)
PCIe
Packet buffers
Ax & Bx (emulated)
Rx (non-emulated)
Packet
completion
Ax desc
Rx desc
Bx desc
Notes: We therefore implement rxBisect using a software NIC. In our system, we have two NUMA nodes and NICs are connected at NUMA 0. We run the application’s workers on the NUMA node where the NIC is attached <click>. The workers use emulated NIC Ax and Bx queues that are connected to the emulator, which resides on another NUMA node and hosts non-emulated Rx rings <click>. The packet buffers are located on the same NUMA node as the NIC, which enables the emulator to capture DDIO effects in the same way non-emulated NICs do <click>. For example, when an Ax descriptor is generated <click>, it’s consumed by the emulator and it producers an Rx ring descriptor on the non-emulated Rx ring. Later, when a packet arrives <click>, the NIC writes the packet’s data to buffers on NUMA node 0 <click> and it writes packet completion metadata to the non-emulated Rx ring on NUMA node 1. The emulator converts the completion to a Bx ring entry <click>, which it writes to the emulated Bx ring of the corresponding worker coreon NUMA node 0, thus completing the emulated NIC’s packet processing. We also impelement the baseline private per-core rings (privRing) and shRing using the same emulation techniques. We also impelement the baseline private per-core rings (privRing) and shRing using the same emulation techniques. Our results show that for privRing and shRing emulation throughput is up to 12% lower than non-emulated throughput.

## Slide 19: L3 load balancer (multicore)
Chart: 
privRing | 162.2
small privRing | 195.3368
shRing | 195.7896
rxBisect | 195.3
Throughput (Gbps)
+20%
+20%
PrivRing
Small privRing (impractical)
ShRing
RxBisect
+20%
Notes: To evaluate the performance of rxBisect on a real application we use a stateful load balancer network function, which rewrites packet headers to spread load among 16 servers. We run the load balancer on all cores and load it with 200Gbps. We compare between a default sized private ring per core, which we call privRing, small private rings that fit in DDIO but will cause loss if traffic is bursty, shRing between 8 cores, and rxBisect between 8 cores. The working set of private rings doesn’t fit in DDIO, and hence its throughput is low <click>. Small private rings, shRing, and rxBisect fit in DDIO and hence they reach line rate, improving throughput by 20%. Note that in this experiment, only rxBisect is emulated, and the rest are not emulated.

## Slide 20: L3 load balancer (multicore)
Chart: 
privRing | 1086.8586
small privRing | 96.4899
shRing | 101.101
rxBisect | 113.2
Latency
(µs)
-92%
-91%
PrivRing
Small privRing (impractical)
ShRing
RxBisect
-90%
Notes: When looking at latency, we see that default private rings, which do not reach linerate, have latency of about 1ms, while small private rings, shRing, and rxBisect latency is closer to 100us. The reason for privRing’s high latency is that its Rx ring is full of packets, and so latency consists of the time to process all packets in the ring. In contrast, the reception rings are mostly empty for all other architectures.

## Slide 21: Processing load imbalance
Chart: 
| 0 | 50 | 100 | 150 | 200 | 250 | 300
privRing | 174.8759 | 173.0696 | 172.3013 | 172.6104 | 172.5896 | 172.1438 | 172.4883
shRing/8 | 195.9744 | 195.6924 | 195.5869 | 153.672 | 117.5748 | 96.7979 | 80.6325
dynamic shRing | 195.6628 | 195.7402 | 196 | 182 | 171.9677 | 171.7743 | 171.6665
rxBisect | 196.5671 | 196.6823 | 195.6217 | 196.4926 | 193.4166 | 193.0237 | 192.651
Throughput (Gbps)
privRing
shRing
dynamic shRing
Overhead on target core (mem refs per packet)
rxBisect
Notes: Last, we look at the performance under processing load imbalance. To that end, we run a synthetic NF on all CPU cores. Each core accesses memory twice per packet except one core, which we call the target core. On the target core, we vary the number of memory accesses between 0 and 300. We load our app with 200Gbps that is spread evenly among all cores except the target core which receives a very small portion of traffic; only 1% of all traffic. We plot the throughput of our app as a function of the number of memory accesses on the target core. <click> With private rings, the app cannot achieve line rate because its working set is too big, and it performs similarly regardless of the load on the target core. This is expected because 99% of all traffic is being processed by cores other than the target core. <click> In contrast, shRing achieves linerate when the overhead on the target core is low. But, when the load on the target core exceeds 100 memory accesses per packet, shRing performance starts dropping, this happens because the slow target core prevents other cores from making progress <click>. Dynamic shRing heuristically identifies the load imbalance and switches to private rings instead <click>. RxBisect is the only architecture that achieves linerate at the most imbalanced point <click>, demonstrating that rxBisect provides a small working set by efficiently sharing buffers during load imbalance.
Synthetic NF running on all cores
200Gbps load
Target core processing varies between 0—300 mem accesses
Dynamic shring switches to base upon pathological imbalance
Synthetic workload: 2 memory accesses per packet

## Slide 22: Conclusions
Too many receive ring buffers degrade performance
Reducing ring size causes loss when traffic is bursty
ShRing alleviates this, but only when load is balanced
Disentangling receive rings addresses the problem even when load is imbalanced
Notes: In conclusion, the I/O working set imposed by default sized receive rings is too large to fit in the LLC, degrading application performance. Reducing Rx ring size cannot address this problem, as rings as large as the default are necessary to absorb burst traffic. ShRing provides a solution that works only when traffic is balanced, while also requiring software synchronization at all times. We show that by disentangling receive rings, we can share Rx ring buffers with no software synchronization, thus overcoming the drawbacks of shRing.